## Slide 1: Front End for a Magnetic Transmitter
Team #9
Aethan Cubitt
Ben Jarrin
Jacob Janson
External Supervisors
Dr. Jean F. Bousquet
Dr. Parisa Rangraz
Internal Supervisor
Dr. Jacek Ilow

## Slide 2: Presentation Overview
Background
Project Overview
System Architecture
System Verification
Project Planning
Testing & Results
Analysis & Discussion

## Slide 3: Problem Statement
We aim to establish underwater-to-surface communication using Magnetic Induction. This requires generating and transmitting a strong, clean analog sinusoidal signal via a large induction coil to create a changing magnetic field. The current through the coil shall be 5 Amps.

## Slide 4: Project Overview
Signal
  Sine waves at 100 Hz, 1kHz, and 10kHz
  Transmitter
  Under water and ice
  Amplifier
Receiver (out of scope)
  Above ice
  Amplifier and filter
  Quantum
Notes: We want to be able to send a signal of 10kHz (max 30kHz) to through ice and water from below to a receiver above the ice.
We will have a transmitter below the water (at the Dal Aquatron which will be described later) to send MI waves through the water to the receiver which will filter and amplify the signal.
Eventually, the receiver will incorporate superconductors but that is outside of what we are doing for this project.

## Slide 5: Goals & Deliverables
To transmit a sine wave from underwater to above the surface.
  FPGA
    Signal generation
    Capacitor bank control
  Transmitter PCB
    Analog to pulse width modulation of signal with amplification to 125 Watts
    Low Pass filter circuit with inductor as load
    Capacitor switching bank in series with load
    Power management
Notes: To transmit the magnetic wave through water the following subsystems are required.

## Slide 6: System Architecture
FPGA
H-Bridge
Low Pass Output Filter
Transmitter Coil
Transmitter PCB
Capacitor Bank
Analog to PWM

## Slide 7: FPGA System Architecture
User Input
Signal Generator
Capacitor Control
Pin Out
Pin Out
Pin Out
Signal

## Slide 8: Proposed Solution

## Slide 9: FPGA Design
Board: Zybo Z7-10
The two HDL modules will output the following:
1. Signal for 100Hz, 1kHz, or 10kHz
2. Capacitor control to match the signal choice
The FPGA output is fed into the TPA3255 PCB

## Slide 10: Transmitter: Amplifier
Amplifies the FPGA analog signal to 125 Watts – 5 Amps
Uses the TPA3255 Class D audio amplifier, to boost a small analog signal to a large Pulse Width Modulated (PWM) signal
The TPA3255 has been repurposed from an audio amplifier, to combine the encoding signals for the H-Bridge, and the H-bridge itself

## Slide 11: Simulated Amplifier Circuit

## Slide 12: Low Pass Output Filter & Coils
Load is a large inductor.
The low pass filter takes output PWM signal and creates a smooth voltage wave with 5 Amps of current across the load.
Coil Size increased from AWG 24 to AWG 20 to safely support current output.

## Slide 13: Receiver
Second stage of receiver.
Incorporates a low-noise amplifier, inverting amplifiers, and filters in a cascaded configuration.
Purpose: amplify signal picked up by coils and filter out noise introduced in the channel for successful detection by the processor.
Works with +-12V dual power supply for testing and with 24V automotive d-cell lithium batteries.

## Slide 14: Team Structure
Project Manager
Aethan Cubitt
Responsibilities
Time management
External point of contact
LP Output Filter
H-Bridge Amplifier
Software Lead
Jacob Janson
FPGA block coding
Quantum input handling
User interface
Hardware Lead
Ben Jarrin
Amplifier PCB design
Receiver circuit design
LP Output Filter
H-Bridge Amplifier

## Slide 15: High-level Project Schedule
Winter
Design and modelling of receiver
Sept-Oct
FPGA Design
Test System Integration
System Assembly
Amplifier Design
Amplification Literature Review
LP output Filter Design
Nov-Dec
PCB Design

## Slide 16: Project Schedule

## Slide 17: Materials Breakdown
Materials from previous years
FPGA board
Measurement equipment
Receiver
Materials acquired
20 AWG Wire
Amplifier PCB printing and components
Lab computer

## Slide 18: Budget Summary
Item | Cost per item ($) | Quantity | Cost ($)
PCB Board & components | 250 | 1 | 250
New computer | 1500 | 1 | 1500
Total Initial Budget of $1000
Current estimated cost $1750
Notes: https://www.ibuypower.com/store/rdy-trace-7mp-009

## Slide 19: Safety
Working with up to 25 Volts at 5 Amps
To achieve a safe design, we:
Increased coil wire gauge
Added a protective cover over high-power circuit
Built in a fuse to protect from over current
This is medium voltage and requires mandatory safety measures:
Flame resistant (FR) clothing
Smock
Hand and eye protection

## Slide 20: Simulation Test Results
The low pass filter flattens high frequencies and allows our targeted frequencies through.

## Slide 21: Simulation Test Results
3.00
-3.00
The low pass filter successfully filters the PWM input

## Slide 22: Receiver V1
Low-pass filters with 30kHz cutoff frequency.
First-order RC and third-order RLC filters have been simulated for comparison.
Bandpass filter to be considered 100Hz – 30KHz passband.
RC Filter Frequency Response
3rd Order RLC Filter Frequency Response

## Slide 23: Receiver V2
Sixth order active Chebyshev filter with 30kHz cutoff frequency.
Improved frequency response by decreasing the overshoot.
Decrease in overall amplification to better suit signal needs.

## Slide 24: PCB Power Management Schematics

## Slide 25: Verification & Testing Plan
Select 100Hz, 1kHz, and 10kHz to send through PCB
Send signal from 5m away from the receiver
Measure the output of the amplifier to confirm minimal noise through the newly built receiver
Receiver outputs will be read to an oscilloscope

## Slide 26: Critical Analysis & Recommendations
The resistor in parallel reduces the amount of power that reaches the transmission coils by more than 50%
Encoding the PWM H-Bridge signals on the FPGA would allow for more PCB design control
Testing of the system should be done first in a dry lab, followed by Dalhousie’s Aquatron

## Slide 27
Thank You